# Target work programme after BENE and MERIT:

# A Proposed NF-IDS and EUROnu Targets Work Programme

Chris Densham 	2 December 2008

## 1	Basis of Work Programme

The NF-IDS target task will focus as a priority on the issues related to the Neutrino Factory baseline target technology coupled to the baseline primary proton beam and pion capture system. That is a liquid mercury jet and an associated recirculation system; the proton-beam/mercury jet interaction region including a beam dump and the collection of nested solenoids that collects the pions and produces a pion beam with a large energy spread in three 2 ns bursts. The technical programme will use as a basis the work carried out for ‘Neutrino Factory Study 2’, carried forward with a work list volunteered by attendees at a High Power Targets workshop held at Oxford 1-2 May 2008 and at Princeton 6-7 November 2008:

http://www.physics.ox.ac.uk/users/peachk/HPT/Talks.htm

http://www.physics.princeton.edu/mumu/target/

The EUROν design study will include target research for both a Superbeam and a Neutrino Factory. The EUROnu target study is foreseen to include assessments of solid graphite, solid metal, flowing powder and a liquid mercury jet as potential target technologies. These will need to be assessed in terms of integration with a magnetic horn for a SB and a solenoid for a NF. With this input, the NF-IDS task can be broadened to include these alternative technologies leading to a reassessment of the baseline target technology for both types of facility at the conclusion of the report.

## 2	Basis of Cost Estimate

In order to achieve the stated requirement of a cost estimate to 50-75%, it will be necessary to:

- Determine the scope of the costing and division of responsibilities with the rest of the facility, e.g.

  - Scope: build only; build and operate; or build, operate and decommission

  - Envelope definitions with proton driver and muon front end

  - Level of detail required for civil engineering specifications etc

  - Regulatory issues and costs – site specific

- State basis of estimate with reference to above scope

  - statement of assumptions, effect of location, existing infrastructure etc.

  - use of previous studies and facility costs e.g. SNS, J-SNS

- Determine cost model

  - Pricing model for civil engineering, building, materials, construction, installation and commissioning

  - Shared infrastructure costs

  - Costing of institute staff

- Assess uncertainties, contingency

  - Technical risks and cost implications

- Cost implications for alternative target and beam dump technologies

## 3	Selection criteria for choice of target technology for a Neutrino Factory and a Superbeam

|  | Criteria | Driving factors | Inputs & Issues (Nufact) | Inputs & Issues (Superbeam) |
| --- | --- | --- | --- | --- |
| 1. | Performance (I) Pion production and capture efficiency | Material Z Beam-target interaction geometry | High Z favoured | Target diameter and performance as function of material Z |
| 2. | Performance (II) Proton beam parameter limits (energy, power, pulse structure) |  | Baseline accelerator parameters 4 MW, 10±5 GeV | Baseline accelerator parameters SPL: 4 MW, 3-5 GeV CERN PS2: 4(?) MW, 30-50 GeV |
| 3. | Performance (III) Engineering practicality, reliability | Integration with capture system Integration with beam window Integration with Beam Dump Remote Handling complexity Maintenance intervals Failure scenarios Consequences of target failure Time to repair/replace target system | Integration with capture solenoid Near or far dump? | Magnetic horn outline design geometry Far dump |
| 4. | Cost | Target system active volume – civil engineering, shielding and building costs Remote handling complexity Target replacement and disposal cost Target replacement and disposal frequency | Need cost models: SNS, JSNS costs | Need cost models: T2K costs |
| 5. | R&D requirements (I) Off-line | Feasibility, reliability Time and investment | MERIT@ORNL RAL shock tests RAL powder jet plant |  |
| 6. | R&D requirements (II) On-line | beam interactions with materials radiation damage radiochemistry | Need to use existing facilities: MERIT@CERN, SNS, JSNS | Need to use existing facilities: T2K, BNL, FNAL(AP-0) |
| 7. | Regulatory, safety, environmental issues | Liquid metal, solid, powder Site | SNS, J-SNS, Eurisol experience | SNS, J-SNS, Eurisol experience |

## Neutrino Factory Target System Work Programme

NB This is a call for volunteers!

| Baseline liquid mercury target and beam dump | Milestones Dd/mm/yyyy |
| --- | --- |
| Initiate costing based on Nufact Feasibility Study II work and incorporating actual costs of SNS and JSNS and other relevant facilities, involving estimating: |  |
| Active volume of target station |  |
| Mass and cost of steel and concrete shielding |  |
| Cost of solenoid system |  |
| Cost of civil engineering, building and services |  |
| Cost of mercury system |  |
| Cost of remote handling systems including shielding required |  |
| Any other significant costs |  |
| Beam window study |  |
| Incorporate HARP data into MARS/FLUKA simulations |  |
| Pion/muon acceptance studies |  |
| Continue analysis of MERIT data on proton beam/liquid metal jet interactions |  |
| Extend MERIT MHD simulations |  |
| Mercury nozzle studies |  |
| Mercury erosion experiments for bore & nozzle |  |
| Baseline liquid mercury beam dump, decay solenoid and shielding system studies including: |  |
| Beam interactions with liquid beam dump, options for mitigation of splashing, erosion etc |  |
| CFD studies of mercury jet interactions (splash) with dump & containment |  |
| Studies of irradiation, heat loads and cooling of decay solenoid |  |
| Heat loads and cooling of shielding |  |
| Develop engineering layouts for target station including: |  |
| Mercury handling and recirculation system |  |
| Beam windows + remote maintenance |  |
| Integration of mercury jet with capture solenoid, containment and shielding including concepts for remote maintenance |  |
| Integration of beam dump with decay solenoid, containment and shielding including concepts for remote maintenance |  |

| Alternative target technologies (I) re-circulating solid tungsten target | Milestones Dd/mm/yyyy |
| --- | --- |
| Interpretation of RAL off-line shock tests (VISAR data?) |  |
| On-line tungsten experiments (ISIS? BNL? ISOLDE?) |  |
| Conceptual design for a horizontal axis spokeless solid-target wheel: |  |
| Radiation or water cooling |  |
| Drive & support system |  |
| Beam window integration (or no beam windows) |  |
| 4.2.4 Optimisation of ‘Helmholtz’ type geometry with the goal of minimizing the field dip in the target region. |  |
| 4.2.5 Develop a conceptual structure design for the Helmholtz magnet, which provides an entry/exit route for a solid target. |  |
| 4.2.6 Develop concept for beam dump within solenoid coils |  |
| 4.2.7 Remote dump: investigate the possibility to engineer the solenoid coils in such a way to let the beam pass through a “gap” to reach a remote beam dump. |  |
| Study heating of coils & shielding due to disrupted beam |  |
| 4.2.8 Investigate factors affecting the (huge) inter-coil forces, and how to reduce/handle these. |  |
| 4.2.9 Estimate active volume of system and cost implications for TS shielding |  |
| 4.2.10 Investigate remote handling concepts and cost implications |  |

| 4.3 Alternative target technologies (II) flowing tungsten powder |  |
| --- | --- |
| 4.3.1 Agreed comparison of pion capture efficiency for reduced density powdered target with optimised system including accelerator and target geometry. |  |
| Carry out tungsten powder handling and erosion tests using RAL test plant. |  |
| Develop concepts for integration with capture solenoid, proton beam entry and exit windows of (i) open powder jet and (ii) contained powder jet |  |
| Develop concept for near beam dump involving powder receiver |  |
| Investigate concept for remote beam dump involving gap in capture/decay solenoid system |  |
| Develop concept for complete powder target recirculation system |  |
| Estimate active volume of system and cost implications for TS shielding |  |
| Investigate remote handling concepts and cost implications |  |

## 5	Superbeam Target System Work Programme

There is currently no baseline design concept for a Superbeam target and collection system suitable for operation at a 4MW proton beam power. Consequently the first stage of this Work Programme will be to consider the 3 currently foreseen candidates and determine a baseline. A costing will then be determined of this baseline. There is direct synergy for much of this work with the Neutrino Factory work programme described above.

| Static graphite target |  |
| --- | --- |
| Develop new engineering designs and assess physical limits and expected lifetime of static graphite targets |  |
| Investigate heating, shock wave and radiation damage effects of secondary particle interactions with magnetic horn |  |
| Determine effects of beam parameters (beam energy, pulse length) on engineering performance (above) of target and horn system |  |
| Beam window study (NF synergy and generic for SB) |  |
| Investigate target station concepts for integration of static graphite target within magnetic horn, including rapid target replacement |  |
| Investigate potential beam dump concepts as function of beam energy |  |

| Flowing powder target |  |
| --- | --- |
| Investigate possible powder materials in terms of pion production, secondary particle loads on magnetic horn (c.f. graphite) |  |
| Carry out candidate powder handling and erosion tests using RAL test plant |  |
| Develop design concepts for integration of contained powder jet with magnetic horn, proton beam entry and exit windows |  |
| Study heating and cooling of powder pipe wall |  |
| Develop concept for complete powder target recirculation system (NF synergy) |  |
| Investigate target station concepts for remote maintenance |  |

| Mercury jet target |  |
| --- | --- |
| Investigate chemical compatibility of open mercury jet with aluminium magnetic horn |  |
| Interpret results of MERIT experiment for magnetic horn |  |
| Investigate heating, shock wave and radiation damage effects of secondary particle interactions with magnetic horn (c.f. graphite) |  |

| Baseline target choice |  |
| --- | --- |
| Review above options and select target technology baseline |  |
| Carry out cost estimate of target station for baseline technology choice |  |